## Slide 1: Oregon Environmental Laboratory Conference: How DEQ Uses Analytical Data From Point Sources to Protect Water Quality
Spencer Bohaboy Policy Development Specialist
Water Quality Policy

## Slide 2: Introduction
Permit Development Process
  Reasonable Potential Analysis
  Water Quality Based Effluent Limits
Permit requirements
  Schedule A & B
Compliance
Gap analysis and other data requests

## Slide 3: Introduction
Mostly will be talking about facilities >1 MGD
  Major Facilities
Facilities < 1 MGD require a lot less in terms of permit development and analytical monitoring
  Minor Facilities

## Slide 4: Permit Development Process
Reasonable Potential Analysis
  A site specific water quality-based evaluation that models the impacts of a discharge on the receiving water body
  Uses various water quality models to evaluate water quality criteria for toxicity, temperature, pH, dissolved oxygen, ammonia, etc.
  Effluent Data
    Conventional: Normally semi-continuous Chlorine, Ammonia, BOD, TSS, etc. data
    Toxics: Normally 4 Priority Pollutant Scans (>170 parameters)
    Copper and Aluminum BLM: Cu and Al plus a suit of conventional paramaters
  Ambient Data
    Determine site specific water quality criteria: hardness, pH, temp., phosphorous, conductivity, etc.
    Calculate assimilative capacity: Indicated pollutant parameters
  Develops a worst case scenario and determines if there is a reasonable potential that the water quality standards are exceeded at the edge of the mixing zone (if applicable)
Notes: Trying to set up the current atmosphere in the Water Quality Program and point out what will affect laboratories
Data is one of the major themes. As permits grow increasingly more complex, the availability of good data becomes a key factor in being able to issue a permit in a timely manner.

## Slide 5: RPA Example: RP Deter. Toxics

## Slide 6: Permit Development Process
Effluent Limits
  Where “Reasonable Potential” is determined, limits are required
  TBELs: Technology Based Effluent Limits serve as the minimum amount of treatment for conventional parameters
  WQBELs: Water Quality Based Effluent Limits reflect an evaluation of both the discharge and the receiving water body to meet water quality standards
    Effluent flow rates, pollutant concentrations, ambient flow rates, pollutant concentrations
  Other: Some times there are other effluent limits developed from WET test, from basin standards, TMDLs or industrial sector requirements
Schedule A of the Permit

## Slide 7: RPA Example: WQBEL Calculation

## Slide 8: Permit Requirements
Schedule A
  Discharge Compliance limits
    Conventional parameters: TSS, BOD, pH, Bacteria, Chlorine, Ammonia
    Specific parameters where criteria might be exceeded: Toxics
  Ground water, recycled water and biosolids limits
  Mercury Minimization Plan requirements

## Slide 9: Schedule A

## Slide 10: Permit Requirements
Schedule B
  Monitoring requirements to both determine compliance and characterize effluent/ambient for future permit development
  Information regarding required minimum analytical limits
    Analytical Limits are very important since in many cases they become the default effluent limits
    Need to report both Quantitation Limits (MRL) and Detection Limits
  Getting much more data intensive in a short period of time
    From a minimum of 4 data points, now often ask for 10 or more
    Copper and Aluminum Biotic Ligand Model
    Site specific criteria for ammonia, dissolved metals, Copper and Aluminum
  Can be submitted in a variety of manners
    E-reporting
    E-reporting with attached spreadsheets
    Electronic Data Delivery: Cd’s of data to DEQ Lab

## Slide 11: Schedule B

## Slide 12: Schedule B

## Slide 13: Compliance
For each effluent limit in Schedule A, the permittee collect monitoring data and submits to the department
  Past (partial present): Submit monitoring data on paper Discharge Monitoring Reports
    The DMRs would get keyed into the DEQ database by hand to determine compliance
  Present: Submit monitoring data directly to DEQ/EPA database (EPA-Net)
    Minimizes “fat finger” errors and is more efficient
    Allows for laboratories to direct submit data pending client review and e-signature

## Slide 14: Gap Analysis and Other Data Requests
Permitting is a changing environment
  New criteria, TMDLs, water quality listings, federal requirements, etc. often mean that permit writers need data that is not included in the current permit
  Permit backlog often means that data collected for a facility might not be appropriate in terms of size of data set or analytic limit
  Department is working on a formal “gap analysis process” to identify where additional data is necessary
  Department currently has informal processes to identify additional monitoring requirements
    Tier II monitoring
    Permit writer discretion
  Permit writer will issue the permittee a letter or order requiring additional monitoring

## Slide 15: RPA Example

## Slide 16: Questions
Spencer Bohaboy
Policy Development Specialist
Water Quality Permit and Policy Development
503-229-5415
Bohaboy.Spencer@DEQ.state.or.us