## Slide 1
EPA Region 10
Alternate Test Procedures and Method Update Rule
EPA Region 10 – Quality Assurance Manager, Donald Brown

## Slide 2
Quality Assurance Manager
Notes: RQAM:
  Responsible for overseeing the Regional quality system
    Two-tiered: Data Integrity and Scientific Integrity

## Slide 3
RQAM Role
Quality System Oversight and Policy Implementation
Regional Quality Management Plan
QA Team – 4 QA Chemists
Quality System Reviews
Notes: QMP: Regional document that includes several elements to ensure that data integrity as well as scientific integrity are at the foundation of the work EPA does.
QA Team:
  QAPP reviews – QA approvals required for internal, grant, contractor projects
  Data Validation – review data
  Laboratory Requests – MEL, CLP
  Project QA Planning – DQO development, QAPP development
QSR: Review of the quality system for states that have delegated authority.

## Slide 4
RQAM Role
Data Integrity
Quality Assurance Project Plans
Standard Operating Procedures
Quality Assurance Field Activities Procedures
Data Management
Alternate Test Procedure Coordinator
Notes: QAPPs:
A document that describes the necessary QA, QC, and other technical activities that must be implemented to ensure the results of the work performed satisfy the stated performance objectives
EPA requires that all projects involving the collection or use of environmental data must have a QAPP.
QAPPs must be written and approved prior to any data collection or use activities
SOPs:
Written document that gives precise descriptions of routine procedures
Ensure consistency and conformance with organizational practices
QAFAP:
Guidelines to establish QMS to support field activities based on ten operational guidelines to ensure consistency and reduce vulnerabilities. Currently required for EPA personnel/programs and for new/renewed contracts as of FY15.
Data Management:
Scribe is a requirement for data management
All samples collected for and by the Region are required to use Scribe
Data management plan outlined in QMP

## Slide 5
RQAM Role
Scientific Integrity
Scientific Integrity Policy
FEM Competency Policy
Peer Review Policy
Science Inventory
Authorship Policy
Clearance Policy
Public Access Policy
Notes: Scientific Integrity Policy:
Adherence to professional values and practices when conducting, communicating, supervising, and applying scientific results
Applies to all EPA employees, contractors, grantees, volunteers, and collaborators
FEM Competency Policy:
EPA policies require that personnel generating environmental data, such as EPA laboratories, field samplers, and those taking environmental measurements, are competent to do that work.
This requirement is extended to all acquisition and assistance agreement recipients (>$200K)
Peer Review Policy:
EPA policy states that all scientific and technical information that is intended to inform or support Agency decisions is expected to undergo peer review.
Influential scientific information, including highly influential scientific assessments, must be entered into the Science Inventory, to ensure peer review protocol is documented and publicly accessible.
Authorship Policy:
EPA policy requires that employees represent and acknowledge the intellectual contributions of others in published work, such as journal articles and technical reports, and refrain from taking credit for work with which they were not materially involved.
Clearance Policy:
Process of obtaining management approval prior to a work product’s release or publication
Required for both EPA-disseminated scientific products and other scientific products developed as part of an EPA employee’s official duties
Public Access Policy:
Any research publications resulting from EPA-funded scientific research must be made publicly available within one year of publication.

## Slide 6
What is CWA ATP?
40 CFR 136.4 and 136.5
New Method
Alternate Test Procedure
Notes: Clean Water Act Alternate Test Procedure (ATP) program is described at 40 CFR 136.4 (nationwide-use) and 136.5 (limited-use).
Why no drinking water ATP? DW ATPs can only be approved at the national level.
ATP may fall into one of two categories:
  New Method: A method using a determinative technique different from that in an existing Part 136 method.
  ATP: A modification to a Part 136 method that falls outside the scope of the modification flexibility described in the Part 136 method or at 40 CFR 136.6

## Slide 7
ATP Protocols
Protocol for Review and Validation of Alternate Test Procedures for Regulated Organic and Inorganic Analytes in Wastewater Under EPA’s Alternate Test Procedure Program (February 2018)
Protocol for Review and Validation of New Methods for Regulated Organic and Inorganic Analytes in Wastewater Under EPA’s Alternate Test Procedure Program (February 2018)
EPA Microbiological Alternate Test Procedure Protocol for Drinking Water, Ambient Water, Wastewater and Sewage Sludge Monitoring Methods (September 2010)
Updated in 2018
Notes: EPA finalized protocols in 2018 for the review of ATPs and new methods for chemical analytes based on public comments submitted on the 2016 draft protocols.

## Slide 8
ATP Approval Process Overview
Notes: First order of business, determine the intended use of the method (limited-use or nationwide-use)
  This will ultimately determine approval path and method validation requirements
Nationwide-use ATPs are submitted to EPA HQ, Lemuel Walker – Clean Water Act ATP Coordinator

## Slide 9
ATP Method Validation
Tier 1
For use by one laboratory in one or more matrix
Tier 2
For use by all laboratories nationwide for one matrix type
Tier 3
For use by all laboratories for all matrix types
Requires successful single-laboratory testing
Requires successful three-laboratory validation study
Requires successful nine-laboratory validation study
3 Tiered Approach
Notes: Level of Use:
  Tier 1 – Limited Use for Wastewater
  Tier 2 – Nationwide Use in a Single Wastewater Matrix Type
  Tier 3 – Nationwide Use in All Wastewater Matrix Types
Application for Tier 1 submitted to EPA Regional ATP Coordinator
Application for Tier 2 and 3 submitted to National ATP Coordinator at EPA HQ

## Slide 10
ATP Application
Completed Application Form
Justification for ATP
Method in EPA Format
Validation Study Plan
Method Comparison Table
Validation Study Report
Notes: EPA highly recommends that the method developer consult with ATP staff concerning their proposed candidate method and its justification prior to extensive method development. Candidate methods that are insufficiently justified will not be considered further.
EPA recommends that validation study plans are submitted for review and comment to EPA prior to proceeding with ATP validation.

## Slide 11
Confidential Business Information
All information provided to government is subject to FOIA
Any part of application considered proprietary must be marked as “business confidential”
CBI must be submitted as hardcopy and cannot be submitted electronically
Notes: In accordance with 40 CFR 2.203, a business that submits information to EPA may assert a business confidentiality claim covering the information by placing on (or attaching to) the information at the time it is submitted to EPA, a cover sheet, stamped or typed legend, or other suitable form of notice employing language such as trade secret, proprietary, or company confidential.

## Slide 12
Flexibility to Modify Methods
40 CFR 136.6
Modifications to approved test procedures that do not change underlying chemistry or determinative technique allowed
EPA does not issue approval letters for these types of modifications
ATP applications submitted for these types of modifications will be returned
Notes: Applicant can request EPA determine the necessity for a full ATP validation.
Applicant must submit completed form, proposed method in standard EPA format, and method comparison table.
EPA will then determine whether a full ATP validation is required or whether the proposed modification is with the allowed flexibility of 40 CFR 136.6.

## Slide 13
Method Flexibility Examples
Modifications that fall under the flexibility at 40 CFR part 136.6
  Changes in pH adjustment reagents
  Changes between manual, flow analysis, and discreet analyzer
  Changes in calibration range
  Modifications that require approval as an ATP or new method
    Changes to the underlying chemistry of an approved method
    Changes to the determinative technique of an approved method
    Changes to methods that measure method defined analytes

## Slide 14
Methods Update Rule
2017 Revisions
Provide increased flexibility to the regulated community
Improve data quality
Updated methods to keep current with technology advances
Address laboratory contamination issues related to the MDL and better account for intra-laboratory variability
https://www.epa.gov/cwa-methods/methods-update-rule-2017
Notes: MUR: EPA promulgated changes to analytical test procedures that are used by industries and municipalities to analyze the chemical, physical, and biological components of wastewater and other environmental samples that are required by regulations under the CWA.
Examples:
  Updates to current methods listed (e.g., EPA method 608 to 608.3)
  Increased flexibility within methods (e.g., EPA method 624 to 624.1)
  Inclusion of approved ATPs (e.g. ,Colilert 18)
  New MDL procedure
    99% confidence that the measured concentration is distinguishable from method blank
    Consistent with TNI standard

## Slide 15
2018 MUR Update?
EPA has begun work on next proposed Methods Update Rule
EPA anticipates proposal by Fall 2018
For new method or method revision considerations, acceptable data packages must be received by May 30, 2018
2018 Update?

## Slide 16
ATP Application Tips
Considering ATP, contact RQAM first
Submit ATP application as early as possible
Submit a complete package
Notes: RQAM can help:
  Ensure ATP appropriate
  Provide proper forms
  Answer questions
  Establish Timeline
EPA extremely resourced challenged, ATPs take time to review and often require involvement of specialist (i.e., laboratory). Getting them early will help make sure that resources can be properly planned to conduct the review (Refer to #1).
Incomplete ATP applications will not be processed until all information has been submitted. These incomplete packages will be put on hold causing significant delays and often resulting in the ATP application moving to the end of the review queue. Region 10 does have a completion checklist for use if requested.

## Slide 17
ATP Application Tips
ATPs for MDPs are a completely different beast
Check 40 CFR 136.6
More
Notes: Method-defined Parameter (MDP) is a parameter defined solely by the method used to determine that parameter (e.g., acidity, alkalinity, color, pH, turbidity, etc.). ATPs that measure MDPs have the potential to change what is being measured; therefore, given this nature, all ATP applications for MDPs must be submitted to the National ATP Coordinator at HQ. EPA Regional authorities can not approve these.
If a modification falls within the flexibility provided at 40 CFR 136.6, the application will be returned to the applicant with no further action. As part of the applicant’s justification, they must clearly explain why the modifications fall outside the scope of Part 136.6. Omission of this will result in application rejection.

## Slide 18
Questions?
Remember, safety first!
Donald M. Brown
USEPA R10 RQAM
Brown.DonaldM@epa.gov
206-553-0717