## Slide 1: Oregon Environmental Laboratory Conference: New NPDES Permit Requirements and Electronic Reporting
Spencer Bohaboy Policy Development Specialist
Water Quality Policy

## Slide 2: Introduction
Things to Ponder
Current Projects
  EDD for facility characterization data
  Ammonia 2013 RPA
  NetDMR Rollout
What is new
  Copper BLM Criteria
What is coming
  Reforms to address permit backlog
    Electronic Data management System
    Data Bridging Project
    Shift from multi-hat permit writers
  Mercury Monitoring

## Slide 3: Things to Ponder
The Water Quality Program is in a state of flux while addressing the backlog of permits, meeting federal electronic reporting requirements and keeping up with changes to water quality criteria
An audit of the permit development process identified “Data Inadequacy” and “Outdated Date Delivery Systems” as major contributors to the backlog
  Data Inadequacy: old data, no data, not enough analytic range, relevant collection locations or wrong time period
  Outdated Data Delivery Systems: no database integration, no access to databases,
The Department now reviews 100% of permits with a quality review before issuance
41% of all permits reviewed will require an additional data request in regards to effluent parameter samples that are out of date, not included in the original permit or are related to a change in rules
Notes: Trying to set up the current atmosphere in the Water Quality Program and point out what will affect laboratories
Data is one of the major themes. As permits grow increasingly more complex, the availability of good data becomes a key factor in being able to issue a permit in a timely manner.

## Slide 4: Electronic Data Delivery
  About a two years old effort
  The idea is to try to simplify the transition of characterization monitoring data between the permittee and the department
    Majors: approximately 4-10 x 190 toxic parameters
    Minor: might just have a
  Permittee sends Excel file of data to DEQ Lab on CD
The Lab processes the Data, QA’s it and convert to format for use in the RPA spreadsheet
New Excel file sent to Permit Writer for RPA
Due to QA or formatting issues it takes between 12 and 18 hours per facility to complete

## Slide 5: Electronic Data Delivery
Now that we are actively QA’ing data, the Problems:
  Permittee’s not
    understanding their Schedule B permit requirements
    requesting the EDD formatting when submitting the samples
    requesting all monitoring requirements to the lab before sampling
    performing required sample handling techniques (clean hands, dirty hands) or correct preservation (EPA 624) for specific parameters
  Some permittees are hand entering data
  Missing analytical parameters: i.e. MDLs
  OLD DATA is cantankerous
Solutions
  Use the Template: https://www.oregon.gov/deq/wq/wqpermits/Pages/Electronic-Data-Delivery-for-Toxics-Data.aspx
  Ask for a copy of Schedule B of the Permit with a Request for Bid
  Ask for any additionally required “Monitoring Plans”
  Contact DEQ Lab: Sarah Rockwell

## Slide 6: 2013 Ammonia Criteria
New criteria (2015) is site specific
  Require ammonia, alkalinity, pH and Temperature data to complete water quality model
Currently, the amount of monitoring required is based upon a facility’s flow capacity
  larger facilities (4 per month) require more effluent monitoring than smaller facilities (1-2 per month)
  More data is always better
Larger facilities might also need ambient data
Some smaller facilities might require additional monitoring requirements (up to 4 per month) to address the 30 day averaging period
Notes: Basic take aways are that there will be an increase in monitoring for ammonia

## Slide 7: NetDMR
EPA’s Electronic Reporting Rule, modernizes reporting for municipalities, industries and other facilities that hold NPDES permits.
The rule requires NPDES permit holders to report information electronically, instead of filing written paper reports. Oregon adopted EPA's two-phased approach, described below:
  Phase I This phase will include Discharge Monitoring Reports and the Sewage/Sludge Biosolids annual program reports.
  Phase II This phase will begin in 2017 and will include other types of NPDES permit reporting. Electronic reporting of Phase II data groups must be fully implemented by Dec. 21, 2020.
The rule does not change what information is required. It only changes the method by which information is provided: Electronic rather than paper-based.
Option for Laboratories to upload data into system, and permittee reviews and validates
https://www.oregon.gov/deq/wq/wqpermits/Pages/NPDES-E-Reporting.aspx
Notes: NetDMR seems to be changing month by month, so if involved keep up.

## Slide 8: Copper BLM Criteria
Biotic Ligand Model: Simulates toxicity on surface area of fish gills
Oregon is the 3rd state to adopt and 1st with a standard RPA process
Complex, site specific water quality criteria requiring paired data sets (effluent + ambient)
Very data intensive modelling
  Min of 12 to 24 sample events with 12 parameters each (paired: effluent & ambient)
  pH, dissolved organic carbon (DOC), temperature, calcium, magnesium, sodium, potassium, sulfate, chloride, and alkalinity
Implementation is still in the Beta phase
https://www.oregon.gov/deq/wq/Pages/WQ-Standards-Copper.aspx
Coming soon: Aluminum and Cadmium

## Slide 9: Copper BLM Criteria
Notes: Here is Schedule B language. Note how collections times can be challenging. i.e. collect at same time.

## Slide 10: Permit Backlog
Two major data projects
  Electronic Data management System (EDMS)
  Data Bridging Effort
EDMS
  Integrated system to serve entire department
  Folds in NetDMR
  5 to 10 years for full development and implementation
Data Bridging Effort
  Interim approach to hobble together available data resources: LASR, AQWMS, EDD, USGS, etc.
  Will incorporate DEQ lab and probably require standardized report formates
  Less than 1 year to implementation
Shift from multi-hat permit writers
  Dedicated compliance specialist
  More focus on laboratory inspections
  More focus on submittal of data

## Slide 11: Mercury Monitoring
Recent legal challenges to an issued permit is changing the way the Department will be implementing our Methyl Mercury water quality Criterion in the Willamette Basin
This will result in significantly more Total Mercury and Methyl Mercury monitoring requirements in permits
  Influent
  Effluent
  Ambient
  Source Reduction
This might also result in more exotic work such as analysis of fish tissue or determination of the potential for methylation
Concerns:
  Problems meeting QLs (0.001 ug/l Total Hg)
  Matrixing
  Equipment blanks
  Cross contamination (i.e. filters, clean hands – dirty hands, clean equipment, reagents)

## Slide 12: Questions
Spencer Bohaboy
Policy Development Specialist
Water Quality Permit and Policy Development
503-229-5415
Bohaboy.Spencer@DEQ.state.or.us